## Slide 1
www.prismjohnson.in
PRISM
Madhya Pradesh (MP)
Prism Johnson Limited
Village : Mankahari, P.O. : Bathia
Distt. : Satna - 485111 (MP)

## Slide 2
Plant Capacity | Unit-1 (1997) | Unit-2 (2011) | Annual
 | MT/Year | MT/Year | MT/Year
Clinker Production | 1.9 | 2.3 | 4.2
Cement Production | 2.0 | 3.6 | 5.6
Prism Johnson Limited

## Slide 3
Chart: 
| Baseline | Target | Assessment
PAT Cycle-1 (Specific Energy Consumption(kcal/kg Cement) | 783 | 749 | 738
PAT CYCLE – I
(2012 -2015)
Focused Area
Clinker Utilization Factor
Fly Ash addition
Pet Coke Consumption
Alternative Fuel Usage
Thermal Specific Energy Consumption
Upto Clinkerisation Electrical SEC
Cement Grinding Electrical SEC
Baseline Year
0.6921
26.80%
0
0
806 kCal/kg Clk.
52.2 kWh/T Clk.
31.6 kWh/T Cem.
Assessment Year
0.6721
29.6%
59.0%
1.6%
770 kCal/kg Clk.
51.9 kWh/T Clk.
32.7 kWh/T Cem.
Prism Johnson Limited : UNIT- I
(kCal/Kg Cement)

## Slide 4
Chart: 
| Baseline | Target | Assessment
PAT Cycle-1 (Specific Energy Consumption(kcal/kg Cement) | 783 | 749 | 738
PAT CYCLE – I
(2012 -2015)
ESCerts - Earned
3700
Saved – (MT)
52
Prism Johnson Limited : UNIT- I
Energy efficiency improvement measures implemented | Energy Savings | Units
By Process optimization reduced Pre Heater exist temp by 10 Deg C. | 1268 | MkCal
Clinker Cooler upgradation to achieve better heat recuperation efficiency | 1706 | Mkcal
Saving of compressed air by 5 % | 684 | MWh
(kCal/Kg Cement)

## Slide 5
Chart: 
| Baseline | Target | Assessment
PAT Cycle-2 (Specific Energy Consumption(kcal/kg Cement) | 732 | 697 | 692
PAT CYCLE – II
(2016 -2019)
Focused Area
Clinker Utilization Factor
Fly Ash addition
Pet Coke Consumption
Thermal Specific Energy Consumption
Upto Clinkerisation Electrical SEC
Cement Grinding Electrical SEC
Baseline Year
0.6721
29.61%
59.0%
770 kCal/kg Clk.
51.9 kWh/T Cem.
32.7 kWh/T Cem.
Assessment Year
0.6432
32.4%
50.0%
751 kCal/kg Clk.
48.9 kWh/T Cem.
28.8 kWh/T Cem
Prism Johnson Limited : UNIT- I
(kCal/Kg Cement)

## Slide 6
PAT CYCLE – II
(2016 -2019)
ESCerts - Earned
1515
Saved-(MT)
47
Prism Johnson Limited : UNIT- I
Energy efficiency improvement measures implemented | Energy Savings | Units
Replacement of conventional lamps with LED & Timer installation | 1095 | MWh
Implemented advanced DCS control to optimize process | 99 | MWh
Replacement of Low efficiency equipments with high efficiency | 1046 | MWh
Installation of VFD at variable speed application to save energy. | 2492 | MWh
Reduce the pulley size in bag filter fans of Raw Mill area | 66 | MWh
Upgradation of Cooler with ABC cooler to improve cooler recuperation efficiency | 13426 | MkCal
Minimize heat loss in tertiary air duct by improving insulation | 4475 | MkCal
(kCal/Kg Cement)
Chart: 
| Baseline | Target | Assessment
PAT Cycle-2 (Specific Energy Consumption(kcal/kg Cement) | 732 | 697 | 692

## Slide 7
Chart: 
| Baseline | Target | Assessment
PAT Cycle-3 (Specific Energy Consumption(kcal/kg Cement) | 746 | 707 | 679
PAT CYCLE – III
(2017 -2020)
Description
Clinker Utilization Factor
Fly Ash addition
Pet Coke Consumption
Thermal Specific Energy Consumption
Electrical Specific Energy Consumption
Baseline Year
0.6817
28.52%
34.0%
770 kCal/kg Clk.
32.7 kWh/T Clk.
Assessment Year
0.6581
30.6%
69.0%
751 kCal/kg Clk.
28.8 kWh/T Clk.
Focused Area
Clinker Utilization Factor
Fly Ash addition
Pet Coke Consumption
Alternative Fuel Usage
Thermal Specific Energy Consumption
Upto Clinkerisation Electrical SEC
Cement Grinding Electrical SEC
Solar energy generation
Baseline Year
0.6817
28.52%
34.0%
0.5%
860 kCal/kg Clk.
56.2 kWh/T Clk.
33.5 kWh/T Cem.
0.0%
Assessment Year
0.6581
30.6%
69.0%
4.7%
752 kCal/kg Clk.
56.4 kWh/T Clk.
32.7 kWh/T Cem.
2.4%
Prism Johnson Limited : UNIT- II
(kCal/Kg Cement)

## Slide 8
Chart: 
| Baseline | Target | Assessment
PAT Cycle-3 (Specific Energy Consumption(kcal/kg Cement) | 746 | 707 | 679
PAT CYCLE – III
(2017 -2020)
Prism Johnson Limited : UNIT- II
Energy efficiency improvement measures implemented | Energy Saving | Units
Replacement of Low efficiency equipments with high efficiency | 510 | MWh
Replacement of conventional lamps with LED & Timer installations | 365 | MWh
By reducing the losses of equipment's | 181 | MWh
Process optimization and Modifications in interlock | 2299 | MWh
Minimize heat loss in tertiary air duct by improving insulation | 2718 | MkCal
VFD drives installation to save energy after change in RPM as per requirement | 428 | MWh
Improve mill ventilation for cement mills and reduce fineness at mill outlet | 55 | MWh
ESCerts - Earned
9492
Saved – (MT)
87
(kCal/Kg Cement)

## Slide 9
Chart: 
| Baseline | Target | Assessment
Unit-I | 684 | 661 | 621
PAT CYCLE – VII
(2022 -2025)
Prism Johnson Limited : UNIT- I & II
Chart: 
| Baseline | Target | Assessment
Unit-II | 718 | 669 | 631
Unit-I
Unit-II
(kCal/Kg Cement)
(kCal/Kg Cement)
Expected Achievement
Expected
Expected

## Slide 10
PAT CYCLE – VII
(2022 -2025)
Prism Johnson Limited : UNIT- I & II
Mitigation Plan
Action are under execution | UOM | U-I | U-II
For 01 Crore kWh Green energy generation, kCal/kg Cement reduced | kCal/kg Cem. | 11.8 | 9.1
For 01% TSR by AFR ,kCal/kg Cement reduced | kCal/kg Cem. | 4.9 | 4.9
WHRS generation | kWh in Cr. | 5.0 | 6.1
Solar generation | kWh in Cr. | 1.2 | 1.2
Wind Power | kWh in Cr. | 2.0 | 1.3
AFR usage | % TSR | 1 | 10
Total reduction of kCAl/kg cem. | kCal/kg cem. | 101 | 128
Target FY 2024-25 as per Cycle-VII | kCal/kg cem. | 661 | 669
Expect to achieve FY 2024-25 | kCal/kg cem. | 621 | 631

## Slide 11
Adoption of Green Power
Sr No. | Description | Capacity
1 | PV Solar Power Plant | 30.4 MW (DC) Own premises Feb-2021
2 | Group Captive Wind (Open Access) | 24 MW Within MP State Dec-2023
3 | Biomass Power Plant (Open Access) | 5.5 MW Within MP State On availability
4 | WHRS | 22.5 MW Mar-2021
With Blend of Solar & Wind formed Hybrid Model

## Slide 12
Step Taken for Green Power
Installed Capacity – 30.4 MW
Land Used 105 Acer
Since Feb 2021
Step to form Hybrid
Being blend with Wind 24 MW
Dec 2023
Notes: Manoj Kumar

## Slide 13
Step Taken for Green Power
Installed Capacity – 22.4 MW
Since Mar2021
Notes: Manoj Kumar

## Slide 14
Year | Grid | CPP+OA Power | Green Power | Step Taken towards Green Power
FY 18-19 | 54% | 46% | 0% | NO – RE Power
FY 19-20 | 41% | 58% | 1% | Installed Solar Plant
FY 20-21 | 46% | 44% | 10% | 30.4 MW DC Solar
FY 21-22 | 27% | 38% | 34% | Added WHRS
FY 22-23 | 61% | 1% | 37% | Solar + WHRS
FY 23-24 | 56% | 0% | 44% | Part Wind Power
FY 24-25 | 48% | 0% | 52% | 24 MW Wind
Chart: 
| FY 18-19 | FY 19-20 | FY 20-21 | FY 21-22 | FY 22-23(upto Nov) | FY 22-23* | FY 23-24* | FY 24-25*
Grid | 0.54 | 0.41 | 0.46 | 0.27 | 0.61 | 0.61 | 0.56 | 0.48
CPP+OA Power | 0.46 | 0.58 | 0.44 | 0.38 | 0.04 | 0.01 | 0 | 0
Green Power | 0 | 0.01 | 0.1 | 0.34 | 0.34 | 0.37 | 0.44 | 0.52
Adoption of RE Electrical Power

## Slide 15
Cycle | Period | Unit | Baseline | Target, | Achieved, | No of Escerts | C02 Reduction (MT) | Total MkCal Saved
PAT-I | 2012-15 | Unit-1 | 783 | 749 | 738 | 3700 | 51 | 147015
PAT-II | 2016-19 | Unit-1 | 732 | 697 | 692 | 1515 | 47 | 133106
PAT-III | 2017-20 | Unit-2 | 746 | 707 | 679 | 9492 | 87 | 248402
PAT-VII* | 2022-25 | Unit-1 | 684 | 661 | 621 |  | 73 | 209634
PAT-VII* | 2022-25 | Unit-2 | 718 | 669 | 631 |  | 113 | 323987
Total |  |  |  |  |  |  | 372 | 1062146
PAT – Achievements
ESCerts - Earned
14707
Saved – (MT)
2012-2020: 185
By FY 2025: 372
Expected
((kCal/Kg Cement))
Chart: 
| 2012 | 2016 | 2019 | 2025
Unit-1 | 783 | 738 | 692 | 621
Chart: 
| 2017 | 2020 | 2025
Unit-1 | 746 | 679 | 631
Unit-1
Unit-2
Notes: Om Prakash Verma

## Slide 16: Benefit of PAT
Major Benefits:
Increase profit margin due to reduce share cost of energy.
Waste heat recovery and solar plant- reduce grid dependency.
Achieved internal environment target.
Helped in achieving group Sustainable Development goals (SDG).
Capacity building in energy efficiency and conservation.
Notes: Om Prakash Verma

## Slide 17: Thanks
Notes:
All shown data are Audited by BEE certified agencies & Auditors.
Reference & BEE Logo taken from BEE official website. https://beeindia.gov.in
Notes: Om Prakash Verma