## Slide 1
Energy Efficiency Journey in Tata Steel
14 Dec 2022

## Slide 2
Policies
Sustainability Pillars
Vision
CSR: Corporate Social Responsibility, HR: Human Resource, POSH: Prevention of sexual harassment, SC: Supply Chain,
ABAC: Anti-Bribery and Anti-Corruption , AML: Anti-Money Laundering; Material issues were identified based on a third-party study in 2018
We aspire to be the global steel industry benchmark for
Value Creation and Corporate Citizenship
Environment
Health, Safety
&
Employee welfare
Community
Governance
Tata Code of Conduct
Environment, Climate Change, Biodiversity, Energy
Health & Safety, HR, Social Accountability, CSR, Affirmative Action, POSH
Responsible SC, ABAC, AML, Data Privacy, Remuneration, Whistle Blower
Sustainability Policy
Material Issues
Environment
Social
Governance
Strategy Development
Strategic Objectives & Strategic Enablers
Leadership in sustainability
Strategy Deployment
Annual Business Plan and Long-Term Plan
Our Approach
Our sustainability framework

## Slide 3: Our carbon footprint is best in class in the geographies we operate in, and our long term decarbonization roadmap is aligned with national commitments
BAT: Best Available Technology, EAF: Electric Arc Furnace, BF: Blast Furnace, NG: Natural Gas, BF: Blast Furnace
Key Enablers
Adoption of BAT
Maximizing scrap use
Raw material quality improvement
Greening of power mix
Scrap based growth (EAF) in India
Reconfiguration of assets – NG/H2 based DRI, Hisarna & CCU/S
Performance Over the Years
Carbon Intensity (tCO2/tcs) of Tata Steel India Operations
Improvement in carbon emission intensity across all locations
  TSJ is a national benchmark
  9% reduction in carbon emission intensity in the new & acquired assets (TSM and TSLPL) in the last 2-4 years
Long term decarbonization roadmap created
Way Forward
Achieve <1.8 tCO2/tcs carbon emission by 2030
Focus on
technology enabled transition to net zero
Consistent focus and investment in green technology
Net Zero by 2045
Climate Change
Chart: 
| FY06 | FY08 | FY10 | FY12 | FY14 | FY16 | FY18 | FY20 | FY22 | FY25
Column1 | 3.11 | 2.66 | 2.5 | 2.5 | 2.47 | 2.3 | 2.37 | 2.49 | 2.51 | 2
Crude steel production (Million Tons)
Incorporates acquired assets
19.01
4.7
20% reduction in carbon emission intensity
Use of alternate reductants in BF e.g., NG, H2, Biochar

## Slide 4: TSL has developed a low carbon transition strategy, spread over three horizons which progressively reduces reliance on fossil fuel, yet allows for growth
Horizon 1: By 2025, Achieve specific carbon emission of around 2 tCO2 per tcs - implement BAT to achieve benchmark levels in energy efficiency and Carbon emissions through BF-BOF route
Horizon 2: By 2030, grow through Scrap-EAF route, improve efficiency of existing assets by augmenting with low emission H2 rich fuels like NG in BFs
Horizon 3: Between 2030 - 2045, decouple absolute CO2 emission from growth by introducing hydrogen and CCUS at ironmaking stage and adding capacity through cleaner technology configurations
  Energy and Process Efficiency measures
  Upgradation of existing facilities with efficient ones
  Expansion with best available technologies
  Invest in renewable energy
  Use of good quality feedstocks
  Growth via scrap based EAF route
  Use of H2 rich gas (e.g., Natural Gas) for tuyere injection
  Carbon Capture & Utilization (CCU) to Methanol and Carbon Capture & Storage (CCS)
  Modifying existing BF assets with CCU/S at next investment cycle
  Offset ‘unavoidable emission’ through Carbon Capture Utilization and Storage(CCUS)
  Green Hydrogen based Direct Reduced Iron + Electric Arc Furnace (DRI-EAF)
  De-carbonise incoming utilities completely
Availability of clean scrap
Access to low-cost green capital
Carbon pricing between 10 – 30 $/ton
Establishing supply chain for scrap availability for EAF
Support of public procurement of low carbon embedded steel.
Retrofitting feasibility of new assets
Access to low-cost green capital
Carbon pricing between 40-100 $/ton
Commercialization of net zero technologies –CCU/S and H2
Market for products utilizing CO2
Support of public procurement of low carbon embedded steel
Low-cost renewable electricity
Abatement
contingent to
Key emission
reduction measures
Transition strategy

## Slide 5
Realised Impacts: PAT Cycle in Tata Steel
Unit | PAT Cycle | Target | Achievement Levels | Escerts Issued | Energy Saving
TSJ | PAT 1/PAT 2/PAT 7 | 0.607/0.5802/0.5620 | 0.581/0.5668 | 40188/125053 | 6.62%
TSLPL Joda | PAT 1/PAT 2/PAT 7 | 0.551/0.5202/0.3881 | 0.5201/0.394 | 20153/36783 | 28.07%
TSLPL Gamharia | PAT 1/PAT 2/PAT 7 | 0.229/1.6324/0.6984 | PAT 2 Cycle: 0.792 | 26543 | 51.48%
TSL Sahibabad | PAT 1/PAT 2/PAT 7 | 0.054/0.0215/0.0170 | 0.306/0.0180 | 15673/25673 | 40.07%
TSL Khopoli | PAT 1/PAT 2/PAT 7 | 0.056/0.0345/0.324 | 0.0340/0.0320 | 24786/18743 | 42.85%
TSM | PAT 3/ PAT 7 | 0.6558/ 0.4921 | 0.524 |  | 20%
FAP Bamnipal | PAT 3/PAT 7 | 0.7696/0.7608 | 0.778 |  | 1%
TSK | PAT 5 | 0.6596 |  |  | 
Chart: Gcal/tcs
| Baseline SEC | Target SEC | Actual SEC
 | 6.46 | 6.07 | 5.96
Escerts issued: 40188 and Escerts traded: 22673
PAT I Cycle for TSJ
Total saving :
Rs1,11,694/tcs

## Slide 6
Benchmark Study on Specific Energy Consumption
A benchmark study on Specific Energy Consumption with World Steel Association (WSA, erstwhile known as IISI – International Iron & Steel Industries) reveals the followings.
The comparison between Tata Steel and WSA is shown below:
Chart: Gcal/tcs
| World Bench Mark | TSJ
 | 4.3 | 5.67
Differentiating factors for calculation between WSA and Tata Steel – Gcal/tcs |  | 
Actual Gap between WSA and Tata Steel | 1.37 | 
Hot-metal/ Crude-steel Ratio ( less use of scrap) | 0.900 | 
Refractories production (own plant) | 0.122 | 
Benzol Recovery ( not available) | 0.079 | 
Purchased Power ( Higher grid efficiency) | 0.080 | 
Coke Ash ( Higher coke ash) | 0.038 | 
Hot-metal Silicon ( Higher silicon in HM) | 0.035 | 
Coal Ash ( Higher ash in coal) | 0.117 | 
Coal Volatile Matter ( Higher VM in coal) | -0.045 | 
Blooming Mills, Sectional Mills and Plate Mills ( N.A) | -0.248 | 
Achievable Gap between TSL & WSA | 0.292 | 
Gap cannot be achieved due to operating conditions and infrastructure

## Slide 7
Best Available Technique in Iron and Steel Sector
Technique | Energy Saving Potential (Gcal/tcs) | Investment (Rs) | Payback Period ** |  | Implemented in TSJ | Implemented in TSK
 |  |  | Without PAT scheme | With PAT scheme |  | 
Waste heat recovery from Sinter bed | 0.028 | 134.4 million | 48 months | 26 months | ꭓ | ꭓ
Improvement in segregated charging of sintering material | 0.029 | 69.60 million | 24 months | 13 months | √ | √
Sensible heat from main exhaust gas of sintering machine | 0.045 | 135 million | 36 months | 18 months | ꭓ | ꭓ
Coal Moisture Control | 0.065 | 193.80 million | 36 months | 18 months | ꭓ | ꭓ
Automated combustion control of coke ovens | 0.054 | 129.60 million | 36 months | 16 months | √ | √
Coke Dry Quenching | 0.28 | 1000 million | 36 months | 8 months | √ | √
Top pressure recovery turbine | 0.07 | 252 million | 48 months | 24 months | √ | √
Pulverised coal Injection | 0.035 | 115 million | 40 months | 20 months | √ | √
**Assumption: Escerts traded @Rs 1700/unit

## Slide 8
Best Available Technique in Iron and Steel Sector (cont…)
Technique | Energy Saving Potential (Gcal/tcs) | Investment (Rs) | Payback Period |  | Implemented in TSJ | Implemented in TSK
 |  |  | Without PAT scheme | With PAT scheme |  | 
Plastic Waste Injection | 0.0407 | 778 million | 36 months | 24 months | ꭓ | ꭓ
Natural Gas Injection | Fuel savings are estimated to be 0.9 GJ/t-HM. | 540 million | 24 months | 18 months | ꭓ | ꭓ
Heat Recuperation from Hot Blast Stoves | 0.3 GJ/t-pig iron | 90 million | 36 months | 18 months | √ | √
Scrap Preheating | 0.016 to 0.2 GJ/t-steel. | 70 million | 12 months | 8 months | ꭓ | ꭓ
**Assumption: Escerts traded @Rs 1700/unit

## Slide 9
Major Barriers in Escerts Trading
Inference
With present rules, ESCerts of PAT cycle 1, if not traded during upcoming PAT cycle 2 trading will expire after PAT cycle 2 compliance period. The expected desperation to sell a commodity, which is set to expire may result in lower MCP for ESCerts in terminal trading sessions
At the end of compliance period of PAT Cycle 2, surplus ESCerts is expected to be 4.57 million ESCerts, which is 80% of the total ESCerts issued during PAT cycle 2.
With present rules, at end of PAT cycle 3 compliance period, approx. 4 million ESCerts may retire without being traded. This volume may go up if compliance is low in DISCOM sector, similar to the case observed in REC market for RPO compliance